## Slide 1: Transport update: Cambridge and South Cambridgeshire COVID-19 transport impacts and recovery
September 2025
Policy & Insight Team, Cambridgeshire County Council

## Slide 2: Transport Update Aims
This report is intended to:
Provide a basis for discussion for the Greater Cambridge Partnership (GCP) to understand and identify existing challenges and future data needs.
Summarise the on-going impacts of COVID-19 on trends in transport and mobility up to 30th September 2025.
Highlight changes in key indicators by comparing September 2025 data to a pre-pandemic baseline (September 2019 or closest possible equivalent), September 2023 and to last year (September 2024).
Due to the availability of comparable data, comparison with pre-COVID levels is not possible for all datasets. Comparison against a 2023 baseline is therefore also provided.
Notes:
Comparison periods may vary across the different datasets based on the availability of historic data – comparison periods are clearly noted for each dataset.
  Where reference is made to ‘Weekdays’ this only includes Monday, Tuesday, Wednesday and Thursday.
  Data from the permanent traffic sensors and Annual Traffic Surveys can also be viewed using our online dashboards.

## Slide 3: Colour scale
The statistics in this pack have been colour-coded using a heat scale to reflect the level of recovery being experienced (pre-COVID compared to now).
A positive (red) value indicates that levels have increased above those experienced pre-COVID.
A negative (blue) value indicates that levels remain below pre-COVID.
Tip:
Look out for the colour scale bar in the top right-hand corner of each page for a reminder of the heat scale used to indicate the level of recovery throughout the pack.

## Slide 4: Accessibility
To access the full functionality of PowerPoint, we recommend opening the slides in full screen mode. To do this, click the “Open in New Window” button in the bottom right-hand corner.
1) Navigate through the slide pack using the left and right arrows in the middle-bottom of the screen. Clicking on the sentence “Slide x of x” brings up a pop-up listing all the slides so you can navigate directly to a slide of interest.
2) Open the Notes for each slide to see the data source, technical notes and any additional commentary. See the “Notes” button in the bottom right-hand corner.
3) Use the “Download” button to the right of the centre at the top of the screen to download the slides as a .pptx file.
4) Use the “Print to PDF” option to save the PowerPoint as a PDF document (but please be aware you will lose access to the Notes section which contains additional information for the slide).
5) Use the “More options” icon in the top right-hand corner and choose “Accessibility mode” from the pop-up menu to access the slides in a different format which will display any Alt Text that has been set for charts and images.
We are continually working to improve the accessibility of our content. If you find you are unable to access any part of this update, please contact policyandinsight@cambridgeshire.gov.uk and we will be happy to investigate providing information in an alternative format.

## Slide 5: Overview

## Slide 6: Recovery Tracker: Has transport use returned to pre-COVID levels?
For all data sources and any other relevant information regarding these metrics, please consult the notes section of this slide.
Figures for 2021 have been obscured to improve the display of this recovery tracker. Figures for 2021 still comprise part of the ‘Trendline’ and are available on request.
Notes: Sources and Geographical Scope:
Retail Footfall: Data Sourced from Cambridge BID. Central Cambridge only
Cycling Trips: Data Sourced from Google Environmental Insights. Cambridge only.
Walking Trips: Data Sourced from Google Environmental Insights. Cambridge only.
Car Parking: Data Sourced from Cambridge City Council. Multi-Storey Car Parks in Central Cambridge only.
Local Road Vehicles: Data Sourced from VivaCity. Greater Cambridge Only – please consult slide pack notes for specific data collection locations.
Strategic Road Vehicles: Data Sourced from National Highways. All of Cambridgeshire – please consult individual slides for specific data collection locations.
Motor Vehicle Trips: Data Sourced from Google Environmental Insights. Cambridge only.
Motor Distance Travelled: Data Sourced from Google Environmental Insights. Cambridge only.
Rail Passengers: Data Sourced from the Office of Rail and Road. Cambridge Station only.
Bus Passengers: Data Sourced from Stagecoach. Cambridge depot only. (“Use” button push methodology – driver estimate)
Park & Ride Passengers: Data Sourced from Stagecoach. Cambridge only. (“Use” button push methodology – driver estimate).
Park & Ride Passengers: Data Sourced from Stagecoach. Cambridge only. (Multiplier methodology – ticket sales estimate).
Guided Busway Passengers: Data Sourced from Stagecoach. Greater Cambridge only.
Air Pollution: Data Sourced from Cambridge City Council. Central Cambridge locations only. NO2 Emissions only.
Technical Notes: Our methodology for analysing the data continues to be refined to react to differing levels of data quality and data gaps. Therefore, you may observe small adjustments to the stats in the latest slide pack compared to previously published versions.
For example:
The method of calculating the strategic road network (SRN) recovery percentages changed in Dec 2022 to include data from a larger number of sites. The SRN percentages have therefore been updated and may not reflect the values presented in previous slide packs for this reason.
The air pollution percentages historically used data from 5 sensors but one of these sensors was removed in April 2022 so the methodology for calculating the air pollution percentages has been adjusted. The air pollution percentages presented here may differ slightly from those in previous slide packs for this reason.
Commentary:
This slide indicates the extent to which each of the transport metrics has recovered over time in comparison to pre-Covid (2019 or early 2020) levels.
Google mobility workplace, Cambridge: Plateaued recovery 31% below pre-Covid in Sept 2022. Data source discontinued in October 2022.
Google mobility workplace, South Cambridgeshire: fluctuating recovery, 11% below pre-Covid in Sept 2022. Data source discontinued in October 2022.
Retail footfall, central Cambridge: fluctuating recovery levels linked to seasonal variations. Currently increasing but still below pre-Covid.
One Station Square footfall: Erratic pattern of recovery over time. Currently some way below pre-Covid. Urge caution with this data - supplier has been asked to confirm reliability following issues during 2024.
Walking, central Cambridge: Data is only available annually through to 2023. Figures show a gradual recovery in walking volumes; albeit with a plateau between 2022 and 2023.
Cycling, central Cambridge: Data is only available annually through to 2023. Figures show a gradual recovery in walking volumes; albeit with a plateau between 2022 and 2023.
Multi Storey Car Parking, central Cambridge: stable trend in the last two years, consistently between 10-20% below pre-Covid.
Vehicle flows on local roads, central Cambridge: stabilizing recovery trend, now consistently 10-15% below pre-Covid.
Vehicle flow on strategic roads, gradually improving recovery trend, now consistently above pre-Covid levels.
Motorised trip volumes in Cambridge (sourced from Google). Data is only available annually through to 2023. Figures show a gradual recovery in motorised trip volumes - with figures showing as above pre-COVID for 2022 and 2023.
Motorised distance travelled in Cambridge (sourced from Google). Data is only available annually through to 2023. Figures show a gradual recovery in distances travelled via motorised vehicles - with figures showing as above pre-COVID for 2022 and 2023.
Railway passenger numbers at Cambridge Station (updated annually to March) – improving recovery trend, but still some way below pre-Covid.
Bus passengers, Cambridge: improving recovery trend from March 2022 to March 2024. Stabilising recovery trend since March 2024, consistently 5-8% below pre-Covid.
Park and Ride passengers (Driver Estimate): consistent recovery trend, now consistently above pre-Covid levels, albeit with some site-by-site variation.
Park and Ride passengers (Ticket Sales Estimate): improving recovery trend, now consistently at pre-COVID levels.
Guided Busway passengers (updated annually): Improving recovery trend but still a little way below pre-COVID.
NO2 emissions: consistently remaining some way below pre-Covid.

## Slide 7: Headlines: September 2025
Local Roads
Volumes at…
…compared to 2019
…compared to 2023.
-1%
-2%
Strategic Roads
Volumes at…
…compared to 2019
…compared to 2023.
+19%
Car Parking
Patronage at…
…compared to 2019
…compared to 2023.
-16%
P
Bus
Patronage at…
…compared to 2019.
…compared to 2023.
Cambridgeshire depots only.
+2%
Park and Ride
Patronage at…
...compared to 2019.
...compared to 2023.
Cambridgeshire depots only.
0% to +19%*
P
+
Retail Footfall
Volumes at…
…compared to 2019.
…compared to 2023.
-4%
+1%
Walking
2023 volumes at…
…compared to 2019.
(Google EIE)
2023 is latest available data.
Cycling
2023 volumes at…
...compared to 2019.
(Google EIE)
2023 is latest available data.
-25%
NO2 Emissions
Concentrations at...
...compared to 2017-19.
...compared to 2023**
-35%
+6%
-16%
+5 to +7%*
+9%
+1%
-2%
Station Footfall
Analysis paused
pending data quality checks.
**Excludes Gonville Place.
*Two different methodologies are available for estimating bus passenger volumes - see Slide 44 onwards for more details.

## Slide 8: Travel Demand

## Slide 9: Is home working here to stay?
The ONS captures the working arrangements of a sample of approx. 800 working adults across Great Britain on a monthly basis. The results suggest that on-site working has gradually reduced since the later stages of the pandemic. Hybrid working has increased since 2020 but has stabilised (32%). Remote working decreased and has now stabilised (16-17%). Census 2021 data suggests that hybrid and remote working is more common in Cambridge & South Cambs than it is nationally.
Year | Percentage of working adults [Great Britain annual average] |  | 
 | On-site working | Hybrid working | Remote working
2020 | 54% | 12% | 34%
2021 | 55% | 14% | 30%
2022 | 58% | 24% | 18%
2023 | 53% | 32% | 16%
2024 | 52% | 32% | 16%
2025 (so far*) | 51% | 32% | 17%
Locally, the 2021 Census (March 2021), demonstrated that levels of remote working in Cambridge (46%) and South Cambs (44%) were higher than the national average (31%) whilst East Cambs (35%) and Hunts (35%) were more similar. Fenland (20%) and Peterborough (25%) were lower than the national average. It is likely that this pattern is a result of the types of employment being undertaken in these areas, with some industries better able to accommodate home working than others. It’s likely that differences between working arrangements across the districts remain today.
Source: Travel to Work Summary
Source: ONS Working Arrangements data for Great Britain. ONS made small changes to the sample of respondents in April 2022 and caution is advised comparing data before/after this date.
On-site working is someone that only worked from a workplace away from home. Remote working is someone who only worked from home. Hybrid working is a combination of working away from home and at home.
*Data available to 28th September 2025.
Notes: Source: ONS Working Arrangements data for Great Britain
Commentary: Data is gathered by ONS who survey a sample of 760 people across Great Britain on a weekly, and more recently motnhly , basis. Some small changes were made to the sample of people surveyed in April 2022 which may have impacted the comparability of data before/after this date. Despite a possible step change occurring in the data at this time, trends post April 2022 continue to suggest a very gradual reduction in on-site workers.

## Slide 10: Is vehicle use increasing?
Estimated motor vehicle miles travelled has gradually increased over time, to over 5 billion miles in 2024. The proportion of miles made by cars and taxis has decreased since 2000 (from 78% in 2000 to 73% in 2024) whilst the proportion of miles made by light commercial vehicles (LCVs) has increased from 16% pre-COVID to 18% in 2024.
Note: The percentage labels represent the split between the different vehicle types (Car and Taxi / LCV / HGV)
 | All motor vehicles | Cars and taxis | Light commercial vehicles | Heavy goods vehicles
Pre-COVID to 2024*: 2019 to 2024 | +6% | +3% | +17% | +7%
2023 to 2024*: 2023 to 2024 | +3% | +3% | +2% | +2%
Source: Department for Transport annual mileage estimates (Road traffic statistics).
Notes: Source: Road traffic statistics - Download data
Commentary: Local authority traffic figures give the total volume (vehicle miles) of traffic across each local authority for the whole year.

## Slide 11: Which methods of travel are being used?
Google collects anonymised location history data from mobile phones to estimate the number of trips and distance travelled by each mode of transport. This data suggests that motor vehicle trips have exceeded pre-COVID levels in all districts whilst active and public transport trips remain below pre-COVID levels, with the exception of South Cambs.
Area | Percentage change in trips (2019 to 2023) |  |  | 
 | Motor Vehicle* | Active Travel | Public Transport | All modes
Cambridge | +6% | -18% | -7% | -8%
East Cambridgeshire | +6% | -9% | -18% | +2%
Fenland | +10% | -10% | -16% | +5%
Huntingdonshire | +1% | -9% | -31% | -2%
South Cambridgeshire | +1% | -12% | +1% | -2%
Cambridgeshire | +5% | -18% | -14% | -4%
*Excludes motorcycle trips due to missing data
Source: Google EIE
All trips entering, exiting and travelling within each area. Data for 2024 not yet released.
Notes: Source: Google Environmental Insights Explorer - Make Informed Decisions
Due to large amounts of missing data, motorcycle trips have been excluded from this analysis. “Motor Vehicle” therefore only includes car trips. “Active Travel” includes walking and cycling trips. “Public Transport” includes bus and rail trips.

## Slide 12: Which methods of travel are being used?
In most districts, the most popular mode choice was motor vehicle with the exception of Cambridge where active travel (walking and cycling) was consistently more popular. For all districts, there is a dip in the number of trips made in 2020 due to COVID-19 and a gradual recovery since then.
No. trips made by mode and year
Source: Google EIE
All trips entering, exiting and travelling within each area. Data for 2024 not yet released.
Notes: Source: Google Environmental Insights Explorer - Make Informed Decisions
Due to large amounts of missing data, motorcycle trips have been excluded from this analysis. “Motor Vehicle” therefore only includes car trips. “Active Travel” includes walking and cycling trips. “Public Transport” includes bus and rail trips.

## Slide 13: How many kilometres are being travelled by each mode?
Whilst a notable number of journeys are made by active travel (walking and cycling), these trips only make up a small proportion of the distance travelled as they are typically shorter in length. Public transport distances exceed active travel distances despite there being fewer public transport trips.
Area | Percentage change in distance (2019 to 2023) |  |  | 
 | Motor Vehicle* | Active Travel | Public Transport | All modes
Cambridge | +5% | -6% | -19% | -3%
East Cambridgeshire | +1% | +5% | -19% | -1%
Fenland | +5% | -0% | -31% | +4%
Huntingdonshire | -5% | +2% | -51% | -9%
South Cambridgeshire | +2% | -10% | -24% | -0%
Cambridgeshire | +1% | -11% | -30% | -3%
Source: Google EIE
All kilometres travelled by trips entering, exiting and travelling within each area. Data for 2024 not yet released.
*Excludes motorcycle trips due to missing data
Notes: Source: Google Environmental Insights Explorer - Make Informed Decisions
Due to large amounts of missing data, motorcycle trips have been excluded from this analysis. “Motor Vehicle” therefore only includes car trips. “Active Travel” includes walking and cycling trips. “Public Transport” includes bus and rail trips.

## Slide 14: How many kilometres are being travelled by each mode?
In each district, cars consistently had the highest total distance travelled. Cambridge and Peterborough (more urban) both had a higher distance travelled using public transport compared to the other districts, perhaps because they are served by a larger number of bus and rail services and because they are employment centres.
Distance travelled by mode and year
Source: Google EIE
All kilometres travelled by trips entering, exiting and travelling within each area. Data for 2024 not yet released.
Notes: Source: Google Environmental Insights Explorer - Make Informed Decisions
Due to large amounts of missing data, motorcycle trips have been excluded from this analysis. “Motor Vehicle” therefore only includes car trips. “Active Travel” includes walking and cycling trips. “Public Transport” includes bus and rail trips.

## Slide 15: Strategic Road Network

## Slide 16: Strategic Road Network Monitoring Sites
Strategic Road Network traffic monitoring sites with continuous data
National Highways have approximately 1,400 permanent traffic monitoring sites on the strategic road network within Cambridgeshire and Peterborough.
Each monitoring site varies in its ability to reliably provide data over time, and periods of inactivity are common. It is therefore not appropriate to conduct comparison between years at all sites.
For comparison to September 2025, there are 45 sites available across Cambridgeshire and Peterborough.
2
N
A47
M11
A11
A14
A14
A1
A428
A14
A1
A1
2
A11
Notes: Source: National Highways WebTRIS data. (https://webtris.highwaysengland.co.uk/)
Sites with data in September 2019, 2023, 2024 and 2025:
SourceSiteDescription District
MIDAS site at M11/6820A Cambridge
MIDAS site at M11/6886A Cambridge
MIDAS site at M11/6886B Cambridge
MIDAS site at A11/0024B East Cambridgeshire
MIDAS site at A11/0041B East Cambridgeshire
MIDAS site at A11/0047B East Cambridgeshire T
MU Site 6317/1 East Cambridgeshire
TMU Site 6350/1 Fenland
TMU Site 6350/2 Fenland
MIDAS site at A1/2033A Huntingdonshire
MIDAS site at A1/2033B Huntingdonshire
MIDAS site at A1/2037A Huntingdonshire
MIDAS site at A1/2037B Huntingdonshire
MIDAS site at A1/2043B Huntingdonshire
MIDAS site at A1/2046A Huntingdonshire
MIDAS site at A1/2046B Huntingdonshire
MIDAS site at A1/2049B Huntingdonshire
MIDAS site at A1/2052B Huntingdonshire
MIDAS site at A1M/2056A Huntingdonshire
MIDAS site at A1M/2115A Huntingdonshire
MIDAS site at A1M/2134A Huntingdonshire
MIDAS site at A1M/2220A Huntingdonshire
MIDAS site at A1M/2228B Huntingdonshire
MIDAS site at A1M/2229A Huntingdonshire
MIDAS site at A1M/2248A Huntingdonshire
MIDAS site at A1M/2254B Huntingdonshire
MIDAS site at A1M/2259A Huntingdonshire
MIDAS site at A1M/2259B Huntingdonshire
TMU Site 6781/2 Huntingdonshire
TMU Site 6782/2 Huntingdonshire
TMU Site 6999/1 Huntingdonshire
TMU Site 6999/2 Huntingdonshire
TMU Site 6351/1 Peterborough
TMU Site 6351/2 Peterborough
TMU Site 6502/2 Peterborough
TMU Site 6503/2 Peterborough
TMU Site 6506/2 Peterborough
TMU Site 7156/1 Peterborough
MIDAS site at M11/6694A South Cambridgeshire
MIDAS site at M11/6743B South Cambridgeshire
MIDAS site at M11/6747A South Cambridgeshire
TMU Site 6310/1 South Cambridgeshire
TMU Site 6312/2 South Cambridgeshire
TMU Site 6314/2 South Cambridgeshire
TMU Site 7123/1 South Cambridgeshire

## Slide 17: Strategic Road Network: Annual Average Daily Flow by Year
In Cambridgeshire and Peterborough, traffic volumes on the Strategic Road Network (SRN) are above pre-COVID levels (+17%) and are slightly ahead of the typical daily flow in 2023 (+3%). However, so far during 2025 there has been a 2% decrease in typical daily volumes compared to 2024.
Pre-COVID to Now:
2019 to 2025
+17%
2023 to Now:
2023 to 2025
+3%
Previous year to Now:
2024 to 2025
-2%
Analysis based on 45 sensors across Cambridgeshire and Peterborough.
Jan-Sept 2025 only
Cambridgeshire and Peterborough
Notes: Source: National Highways WebTRIS data.
Technical note: Average Daily Flow by year for main carriageway monitors in each district. This dataset averages across ALL days (Mon-Sun).

## Slide 18: Strategic Road Network: Average Daily Flow by District
Strategic Road Network flows are higher than in September 2019 in four districts, with only Fenland and Peterborough below September 2019. Huntingdonshire is furthest above 2019 (+36%). Only East Cambridgeshire (+1%) shows higher flows than this time last year (September 2024).
District | Pre-COVID to Now: | 2023 to Now: | Last year to Now:
 | Sep 2019 to Sep 2025 | Sep 2023 to Sep 2025 | Sep 2024 to Sep 2025
Cambridge | +16% | +2% | -7%
East Cambridgeshire | +2% | +1% | +1%
Fenland | -2% | -4% | -3%
Huntingdonshire | +36% | -2% | -7%
Peterborough | -7% | -6% | -9%
South Cambridgeshire | +1% | -0% | -6%
Analysis based on 45 sensors across Cambridgeshire and Peterborough.
Notes: Source: National Highways WebTRIS data.
Technical note: Average Daily Flow by year for main carriageway monitors in each district. This dataset averages across ALL days (Mon-Sun).

## Slide 19: Strategic Road Network: Daily Flow by Day of the Week
On the strategic road network, daily volumes were 19% above pre-COVID in September 2019. However, daily volumes have seen a 7% decrease from September 2024, with this reduction being particularly pronounced at weekends (-15%).
Pre-COVID to Now: |  | 
Sep 2019 to Sep 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
+19% | +17% | +27%
2023 to Now: |  | 
Sep 2023 to Sep 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-2% | +1% | -9%
Previous year to Now: |  | 
Sep 2024 to Sep 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-7% | -5% | -15%
Analysis based on 45 sensors across Cambridgeshire and Peterborough.
Notes: Source: National Highways WebTRIS data.
Technical note: Average Daily Flow in the week for main carriageway monitors in each district. Note the use of ‘normal’ days which allow for a ‘like-for-like’ comparison between comparable days. For example, bank holidays and school holidays are excluded from average flow calculations for ‘normal’ days. As such, this dataset does not account for the Christmas period, Christmas or New Year bank holidays, school summer holidays etc.

## Slide 20: Local Road Network: Daily Flows

## Slide 21: Local Road Network Monitoring Sites
Vivacity Monitoring Sites – Greater Cambridge:
A network of VivaCity sensors is being used to monitor traffic flows across Cambridgeshire. Data from the Greater Cambridge VivaCity sensors (shown on the map) has been used to inform the local road network daily flow analysis presented in this slide pack.
Some sensors have been collecting data for a number of years whilst others are relatively new so the sensors selected to inform each table and chart is based on data availability. For example, relatively few sensors have comparable data stretching back to 2019 so many sensors are excluded from comparisons against 2019.
A list of the sensors included for each piece of analysis is provided in the notes beneath each slide. To access the notes, please view this slide deck in full screen mode by clicking the ‘open in new window’ button (bottom-right) and then click the ‘Notes’ button (bottom-right).
Data from all of the VivaCity sensors across Cambridgeshire can be viewed using the Traffic Flows Dashboard. The locations of all traffic monitoring sites be viewed on the Traffic Count Sites map.
Notes: Source: Cambridge Vivacity sensors
Technical note: This analysis has excluded sensors which may compromise the validity of historic comparisons when figures for all sites are combined. For example, some sites may have data gaps, road closures or events impacting data within the comparison period.

## Slide 22: Local Road Network: Motorised Vehicles
In September 2025, local motorised flows were 1% below pre-COVID levels (September 2019) and have remained stable since 2023.
Average weekday vehicular flow (sum of 41 sites)
Pre-COVID to Now [16 sites*]: |  | 
September 2019 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-1% | -1% | 0%
2023 to Now [41 sites]: |  | 
September 2023 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-2% | -1% | -2%
Previous year to Now [41 sites]: |  | 
September 2024 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-1% | 0% | -4%
*Long-term comparable data available at 16 sites - see the slide notes for the full list of locations. Data from all VivaCity sensors across Cambridgeshire can now be viewed in the Traffic Flows Dashboard.
Notes: Source: Cambridge Vivacity sensors
Technical Notes: 'Non-neutral days' are not included within the calculations.
This chart shows the average volume of motor vehicles counted per weekday for each month/year. We have altered this from previous versions of this slide pack to begin in 2023. This is to enable fuller geographical coverage of Greater Cambridge when comparing motorised traffic flows over time.
There are still 16 sites which provide comparable motorised data in both September 2019 and September 2025; those are listed below; and the comparison between them is shown in the ‘Pre-COVID to now’ table.
The table presents full week and weekend changes against various historic benchmarks to give an indication of how traffic flows are changing.
The comparison figures in the ‘Previous year to Now’ table is generated from data collected at 41 monitoring sites, which are listed below.
Improved data cleaning processes are being developed to improve the omission of any poor quality / non-comparable data.
Commentary:
Motorised traffic flows in 2025 so far are slightly below those observed in 2023 and 2024.
In September 2025, motorised flows are 1% lower than September 2024 overall; albeit with a larger drop in weekdays (-4%) than at weekends (no change).
Motorised flows in September 2025 are 1% below pre-Covid (September 2019). Please note in the site groups list below that this metric is compiled from a different selection of sites to the line chart and the other two year-on-year comparisons.
Sites used to generate line chart, and ‘Previous Year to Now’ summary table:
A10 Ely Road (North of Cambridge Research Park), Arbury Road (just north of Campkin Rd), B1050 Earith Road (north of Willingham), B1050 Hatton's Road (South of Longstanton), Barnwell Road, Beach Road, Boxworth End (south of Rose and Crown Rd), Cambridge Road, Cherry Hinton Road, Chesterton Road (East), Chesterton Road (West), Denny End Road, Ditton Lane (just south of Fen Ditton High St), East Road, Elizabeth Way Bridge, Fen Causeway River Bridge, Gonville Place, Hauxton Road (just north of Trumpington PnR), Hills Road (North), just north of Norwich St, Hills Road Bridge, Hills Road, near Holbrook Road, Huntingdon Road (just west of Storey's Way), King's Hedges Road (just west of Northfield Av), Lensfield Road, Long Road (just west of Sedley Taylor Road), Madingley Road (just east of West Cambridge Site), Mill Road (West), Milton Road SB (north of Cowley Rd, all), Newmarket Road (just east of Ditton Lane), Newmarket Road (just west of Ditton Lane), Pathfinder Way (near The Green), Perne Road, Queens Road, Shelford Road, Station Road, Waterbeach, Tenison Road, Trumpington High Street, Trumpington Road, Victoria Road, Vinery Road, Waterbeach Barracks Access (via Denny End Road).
Sites used to generate ‘Pre-COVID to Now’ summary table:
Cherry Hinton Road, Coldham's Lane, Coleridge Road, East Road, Hills Road Bridge, Histon Road (North), Histon Road (South), Mill Road (East), Mill Road (West), Milton Road (Mid), Milton Road (South), Newmarket Road (just west of Ditton Lane), Perne Road, Station Road, Cambridge, Tenison Road, Vinery Road.

## Slide 23: Local Road Network: Cyclists
In September 2025, cycling volumes were 16% below September 2023 volumes and had reduced very slightly (-2%) over the last year.
Average weekday cycle flow (sum of 46 sites)
Pre-COVID to Now [1 site*]: |  | 
September 2019 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-25% | -25% | -22%
2023 to Now [46 sites]: |  | 
September 2023 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-16% | -15% | -10%
Previous year to Now [46 sites]: |  | 
September 2024 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-2% | -2% | -2%
*Long-term comparable data only available at 1 site (Tenison Road). Data from all VivaCity sensors across Cambridgeshire can now be viewed in the Traffic Flows Dashboard.
Notes: Source: Cambridge Vivacity sensors
Technical note: Bank holiday weeks are not included within the calculations. School holidays are also excluded (except summer holidays in order to obtain figures for August).
This chart shows the average volume of bicycles counted per weekday for each month/year. We have altered this from previous versions of this slide pack to begin in 2023. This is to enable fuller geographical coverage of Greater Cambridge when comparing bicycle flows over time.
Tenison Road only has been used to generate the metrics in the ‘Pre-COVID to Now’ table. This is the only remaining site with comparable data for active modes across this time span.
The table presents full week and weekend changes against various historic benchmarks to give an indication of how cycle flows are changing.
The comparison figures in the other tables are generated from data collected at 46 monitoring sites, which are listed below.
Improved data cleaning processes are being developed to improve the omission of any poor quality / non-comparable data.
Commentary:
In September 2025, cycling volumes are 2% below those seen in September 2024. This pattern is seen at both weekdays and weekends.
September 2025 shows cycling volumes which are 16% below September 2023 overall; with weekdays 15% below 2023, and weekends 10% below.
Across the year as a whole, 2025 cycling volumes are similar to those seen in the last couple of years.
Sites used to generate chart:
Arbury Road (just north of Campkin Rd), B1050 Earith Road (north of Willingham), B1050 Hatton's Road (South of Longstanton), Barnwell Road, Beach Road, Boxworth End (south of Rose and Crown Rd), Cambridge Road, Cherry Hinton Road, Chesterton Road (East), Chesterton Road (West), Coldham's Common (Chisholm Trail), Coldham's Common (Eastern Access near Barnwell Road), Denny End Road, Ditton Lane (just south of Fen Ditton High St), East Road, Elizabeth Way Bridge, Fen Causeway River Bridge, Gonville Place, Guided Busway (Orchard Park), Hauxton Road (just north of Trumpington PnR), High Street, Hills Road (North), just north of Norwich St, Hills Road, near Holbrook Road, Huntingdon Road (just west of Storey's Way), King's Hedges Road (just west of Northfield Av), Lensfield Road, Long Road (just west of Sedley Taylor Road), Madingley Road (just east of West Cambridge Site), Mill Road (East), Mill Road (West), Milton Road SB (north of Cowley Rd, all), Mowbray Road, Newmarket Road (just east of Ditton Lane), Newmarket Road (just west of Ditton Lane), Pathfinder Way (near The Green), Perne Road, Queen Edith's Way, Shelford Road, Station Road, Waterbeach, Stirling Road (near The Green), Tenison Road, Trumpington High Street, Trumpington Road, Victoria Road, Vinery Road, Waterbeach Barracks Access (via Denny End Road).

## Slide 24: Local Road Network: Pedestrians
Average weekday pedestrian flow (sum of 46 sites)
In September 2025, pedestrian volumes were 8% below September 2023 volumes, with a divergence in trend between weekdays (-11%) and weekends (+5%). Pedestrian volumes also show a slight decrease (-4%) compared to this point last year (September 2024).
Pre-COVID to Now [1 site*]: |  | 
September 2019 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
+8% | +6% | +12%
2023 to Now [46 sites]: |  | 
September 2023 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-8% | -11% | +5%
Previous year to Now [46 sites]: |  | 
September 2024 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-4% | -4% | -5%
*Long-term comparable data only available at 1 site (Tenison Road). Data from all VivaCity sensors across Cambridgeshire can now be viewed in the Traffic Flows Dashboard.
Notes: Source: Cambridge Vivacity sensors
Technical note: Bank holiday weeks are not included within the calculations. School holidays are also excluded (except summer holidays in order to obtain figures for August).
This chart shows the average volume of pedestrians counted per weekday for each month/year. We have altered this from previous versions of this slide pack to begin in 2023. This is to enable fuller geographical coverage of Greater Cambridge when comparing pedestrian flows over time.
Tenison Road only has been used to generate the metrics in the ‘Pre-COVID to Now’ table. This is the only remaining site with comparable data for active modes across this time span.
The table presents full week and weekend changes against various historic benchmarks to give an indication of how pedestrian flows are changing.
The comparison figures in the other tables are generated from data collected at 46 monitoring sites, which are listed below.
Improved data cleaning processes are being developed to improve the omission of any poor quality / non-comparable data.
Commentary:
Pedestrian flows in 2025 so far were generally very close to those seen in 2024, until July – when pedestrian flows presented as a little way beneath 2024.
In September 2025, pedestrian volumes are 4% below this time last year. Weekdays are 4% below 2024, whereas weekends are a little further behind (-5%).
September 2025 shows an 8% decrease on 2023 volumes. This is entirely due to a decrease in weekday pedestrian traffic (-11%). Weekends show a 5% increase compared to 2023.
Sites used to generate chart:
Arbury Road (just north of Campkin Rd), B1050 Earith Road (north of Willingham), B1050 Hatton's Road (South of Longstanton), Barnwell Road, Beach Road, Boxworth End (south of Rose and Crown Rd), Cambridge Road, Cherry Hinton Road, Chesterton Road (East), Chesterton Road (West), Coldham's Common (Chisholm Trail), Coldham's Common (Eastern Access near Barnwell Road), Denny End Road, Ditton Lane (just south of Fen Ditton High St), East Road, Elizabeth Way Bridge, Fen Causeway River Bridge, Gonville Place, Guided Busway (Orchard Park), Hauxton Road (just north of Trumpington PnR), High Street, Hills Road (North), just north of Norwich St, Hills Road, near Holbrook Road, Huntingdon Road (just west of Storey's Way), King's Hedges Road (just west of Northfield Av), Lensfield Road, Long Road (just west of Sedley Taylor Road), Madingley Road (just east of West Cambridge Site), Mill Road (East), Mill Road (West), Milton Road SB (north of Cowley Rd, all), Mowbray Road, Newmarket Road (just east of Ditton Lane), Newmarket Road (just west of Ditton Lane), Pathfinder Way (near The Green), Perne Road, Queen Edith's Way, Shelford Road, Station Road, Waterbeach, Stirling Road (near The Green), Tenison Road, Trumpington High Street, Trumpington Road, Victoria Road, Vinery Road, Waterbeach Barracks Access (via Denny End Road).

## Slide 25: Local Road Network: Vehicle Split
Typical weekday flows in September 2025 were lower than those observed in 2023 and 2024, however the vehicle mode split has remained stable.
Average weekday flow (sum of 57 sites)
Active Travel* proportion by year | 
Year | Active %​
September 2023 | 19%
September 2024 | 18%
September 2025 | 18%
September 2025 Top 5 Active Travel Roads (%) | 
Location​ | Active %​
Market Street | 96%
Kingston Street (South) | 93%
St Andrew’s Street | 88%
Devonshire Road (North) | 82%
Hope Street (near Mill Road) | 71%
September 2025 Bottom 5 Active Travel Roads (%) | 
Location​ | Active %​
Boxworth End (S of Swavesey) | 2%
B1050 (N of Willingham) | 1%
Hauxton Road (near P&R) | 1%
A10 (all 3 sites) | 0%
Milton Road (near Cowley Rd) | 0%
*Active Travel includes cyclists and pedestrians.
Data from all VivaCity sensors across Cambridgeshire can now be viewed in the Traffic Flows Dashboard.
Notes: Source: Cambridge Vivacity sensors
Technical Notes:
'Non-neutral' days are not included within average weekday flow calculations.
Fridays are not counted as a weekday. Traffic flows on all other days are counted and used to calculate a typical 'average' traffic flow within central Cambridge on a weekday.
We have selected the most recent month of data (September 2025) and compared it to appropriate periods to show how traffic flows have evolved since these sensors were installed or had their software upgraded.
Previous iterations of this slide pack presented this data going back to 2019 – however, a large proportion of sensors had software upgrades, which meant they had to be removed from the overall comparison.
By September 2024, only two sensors remained with comparable data back to 2019, so we have re-based at 2023.
Commentary
September 2025 data presents with a typical weekday flow of just above 690k across these 57 sites combined - which is a little below the flows seen during September 2024 (700k), and further below September 2023 (724k).
Overall, the proportionate split in travel modes has not changed a huge amount between the three months selected - cars are the dominant mode of transport across Greater Cambridge.
Active modes' share of total flow has remained consistent year-to-year. 18% of total flow on a typical day in September 2025 is made using active modes of travel – which is the same proportion as September 2024 (18%) and just slightly below the proportion seen in September 2023 (19%).
Sites used to generate chart:
A10 Ely Road (North of Cambridge Research Park), Addenbrooke's Road, Arbury Road (just north of Campkin Rd), B1050 Earith Road (north of Willingham), B1050 Hatton's Road (South of Longstanton), Babraham (south of Addenbrooke's Hospital), Barnwell Road, Barton Road (just east of Grange Rd), Beach Road, Boxworth End (south of Rose and Crown Rd), Cambridge Road, Cherry Hinton Road, Chesterton Road (East), Chesterton Road (West), Coldham's Common (Chisholm Trail), Denny End Road, Devonshire Road Cycle Path, Ditton Lane (just south of Fen Ditton High St), East Road, Elizabeth Way Bridge, Fen Causeway River Bridge, Gilbert Road, Gonville Place, Guided Busway (south of Hills Road Bridge), Guided Busway (Trumpington), Hauxton Road (just north of Trumpington PnR), High Street, Hills Road (North), just north of Norwich St, Hills Road, near Holbrook Road, Histon Road (North), Histon Road (South), Huntingdon Road (just west of Storey's Way), King's Hedges Road (just west of Northfield Av), Lensfield Road, Long Road (just west of Sedley Taylor Road), Madingley Road (just east of West Cambridge Site), Mill Road (East), Mill Road (West), Milton Road SB (north of Cowley Rd, all), Mowbray Road, Newmarket Road (just east of Ditton Lane), Newmarket Road (just west of Ditton Lane), Pathfinder Way (near The Green), Perne Road, Queen Edith's Way, Queens Road, Shelford Road, Station Road, Cambridge, Station Road, Waterbeach, Stirling Road (near The Green), Tenison Road, Trumpington High Street, Trumpington Road, Victoria Road, Vinery Road, Waterbeach Access (opposite Cambridge Research Park), Waterbeach Barracks Access (via Denny End Road).

## Slide 26: Cambridgeshire Guided Busway – Active Travel
Cambridgeshire Autumn Survey Sites – Busway Utilisation Monitoring
The Cambridgeshire Guided Busway provides a popular walking and cycling route from St Ives to north Cambridge and within northern and southern Cambridge.
Using Cambridgeshire County Council’s annual traffic survey data, active flows on the busway have been monitored over time at 3 locations:
St Ives Guided Busway – just south-east of the St Ives Park & Ride complex.
Cambridge Guided Busway North – just south of the A14 underpass.
Cambridge Guided Busway South – just north of Trumpington Park Primary School.
Data from 2017 onwards can be seen on the next slide.
Notes: Source: VivaCity

## Slide 27: Cambridgeshire Guided Busway – Active Travel
Autumn 2024 Annual Traffic Survey results showed that total active travel trips along the Guided Busway service path are 17% below pre-COVID (2019) levels; but are 11% ahead of last year (2023). Busway cycle volumes (-12%) are closer to pre-COVID levels than pedestrian volumes (-29%).
Active flows on the Guided Busway
(12-hour flow data from CCC Annual Traffic Surveys)
Pedestrian Flow Change (%)
Pre-COVID to Now:
2023 to Now:
-29%
+28%
Total Active Flow Change (%)
Pre-COVID to Now:
2023 to Now:
-17%
+11%
Cycle Flow Change (%)
Pre-COVID to Now:
2023 to Now:
-12%
+6%
Source: CCC Annual Traffic Surveys. Sum of 3 locations on the guided busway: 1. St Ives; 2. Cambridge – A14 Underpass; 3. Trumpington.
The Annual Traffic Surveys Dashboard provides access to the wider dataset. Note: data is not available for 2022.
Notes: Source: Cambridge Annual traffic surveys

## Slide 28: Local Road Network: Hourly Flows

## Slide 29: Local Road Network: Motorised Vehicle - Annual Survey Sites
Cambridgeshire Annual Traffic Survey Sites
© OpenStreetMap Contributors
Annual Survey Sites
Elizabeth Way
Victoria Avenue​​
Bridge Street
Silver Street
Fen Causeway​​
Histon Road
Milton Road
Horningsea Road
Newmarket Road
High Street (Teversham)
Cambridge Road (Fulbourn)
Worts Causeway
Limekiln Road
Babraham Road
Granhams Road
Shelford Road
Hauxton Road
Coton Road
Barton Road
Madingley Road
Huntingdon Road
Girton Road
Guided Busway (North)
Babraham P&R Entrance
Cambridgeshire County Council commissions annual traffic surveys to determine traffic levels around the county on a “typical” weekday.
The sites shown on this map are those in and around Cambridge at which CCC has collected motorised traffic flows consistently over several years.
Analysis of motorised traffic counts from these sites is presented on the following slide.
Data from the Annual Traffic Survey sites across Cambridgeshire can now be viewed in the Annual Traffic Surveys Dashboard

## Slide 30: Local Road Network: Motorised Vehicle - Peak Spreading
Daily patterns of motorised traffic are starting to resemble the profiles seen pre-COVID (2017-2019), with morning and afternoon peak periods beginning to widen again, albeit still with lower overall volumes (consistently just over 12,000 motorised trips per half-hour compared to just over 13,000 pre-Covid).
Half hour beginning
Note: 2022 excluded due to lack of reliable data. 2025 survey data currently being collected.
Notes: Source: Cambridgeshire Annual Traffic Surveys – Cambridge Radial and Cambridge Screenline . Survey data in 2022 was returned to CCC incomplete, therefore 2022 is excluded as it cannot be presented in comparison to other years.
Technical Note: These figures use the annual traffic survey data from sites in the annual Cambridge Screenline and the Cambridge Radial surveys (only sites which have been consistent across all years). The survey days used in this analysis have been chosen to most closely represent a “typical” day for traffic flows (i.e. avoiding bank holidays, weeks with strike action, other special circumstances which can affect traffic volumes).

## Slide 31: Local Road Network: Active Travel Annual Survey Sites
Cambridgeshire Annual Traffic Survey Sites – River Screenline and Cycle Routes
Sensor Location​​
Elizabeth Way
Victoria Avenue​​
Bridge Street
Silver Street
Fen Causeway​​
Green Dragon Bridge​​
Pye’s Bridge
Fort St George​​
Jesus Lock​​
Garrett Hostel Lane​​
Mill Lane Weir
Coe Fen​
Riverside
Abbey-Chesterton Bridge
Barton Road, Newnham
Cambridge Road, Fulbourn
Cambridge Road, Milton
Cambridge Road, Sawston
Carter Cycle Bridge
Coldhams Lane
Comberton Road
High Green, Great Shelford
High Street, Dry Drayton
Hills Road
Jubilee Way
Long Road
Newmarket Road, Teversham
Oakington Road
Swaffham Bulbeck footpath
Toft Road, Comberton
Quy to Bottisham Footpath
© OpenStreetMap Contributors
Cambridgeshire County Council commissions annual traffic surveys to determine traffic levels around the county on a “typical” weekday.
The sites shown on this map are active travel routes in and around Cambridge at which CCC has collected active travel flows consistently over several years.
Analysis of active travel counts from these sites is presented on the following slide.
Data from the Annual Traffic Survey sites across Cambridgeshire can now be viewed in the Annual Traffic Surveys Dashboard

## Slide 32: Local Road Network: Active Travel Peak Spreading
Morning peak flows remain below pre-COVID levels with the highest volumes between 08:30 and 09:00. Evening peak flows have now exceeded pre-COVID levels with the highest volumes between 17:00 and 18:00.
Half hour beginning
Note: E-scooters were included in these surveys from 2022 onwards and therefore count towards ‘active travel’ in more recent years.
Notes: Source: Cambridge Spring Census – Screenline & Cycle Route Monitoring.
Data Note: In previous versions of this slide pack, totals from both survey days of the Cambridge River Screenline have been included. More recent analysis has only included neutral days to avoid any skewing affect from non-neutral days. Where sites have 2 neutral days of data, the two flows are averaged. Where sites only have 1 neutral day of data, the neutral data is retained and the non-neutral data excluded.
Technical Note: These figures use the annual traffic survey data from the annual Cambridge Screenline and the Cycle Route Monitoring surveys. The survey days used in this analysis have been chosen to most closely represent a “typical” day for traffic flows (i.e. avoiding bank holidays, weeks with strike action, other special circumstances which can affect traffic volumes).
As active travel can be quite variable due to weather conditions, caution is advised using these figures as they are taken from daily surveys rather than calculated over longer periods of time. They are intended to provide a rough indication of trends over time.

## Slide 33: Retail Footfall

## Slide 34: Retail Footfall: Central Cambridge
In September 2025, footfall in central Cambridge was 4% below pre-COVID levels (September 2019) but 8% above this time last year (September 2024).
Pre-COVID to Now: |  | 
September 2019 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-4% | -4% | -4%
2023 to Now: |  | 
September 2023 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
+1% | +1% | 0%
Previous year to Now: |  | 
September 2024 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
+8% | +13% | +3%
Average daily pedestrian footfall: Central Cambridge
This analysis is based on data from 6 locations in Cambridge: Bridge Street, Fitzroy Street, Market Hill, Rose Crescent, Regent Street and Sidney Street.
Notes: Source: Cambridge BID footfall data.
Technical note: Data from the following locations: Bridge Street, Fitzroy Street at Waitrose, Market Hill, Regent Street, Rose Crescent, Sidney Street. Excludes data for King’s Parade and One Station Square. As outlined at the start of this slide pack, 'weekdays' do not include Fridays. Table calculations do not include bank holidays, school holidays or any other "non neutral" days. The percentage changes are designed to reflect change on a "typical" day.
Commentary:
September foot traffic in central Cambridge is 4% below the pre-COVID level of September 2019 and is 8% above September 2024.
Weekday foot traffic (Monday to Thursday) is 13% above last year, whereas weekend foot traffic is only 3% ahead of last year.
September foot traffic is 1% above September 2023.

## Slide 35: Retail Footfall: Central Cambridge by Day of the Week
In September 2025, retail footfall was below pre-COVID levels (September 2019) on most days of the week. Tuesday was the only day above pre-COVID (+2%).
Wednesday is the least recovered day (-13%) whilst Monday and Sunday were similar to pre-COVID levels (0% change).
Average daily pedestrian footfall: Central Cambridge
Pre-COVID to Now: September 2019 to September 2025 |  |  |  |  |  | 
Monday | Tuesday | Wednesday | Thursday | Friday | Saturday | Sunday
0% | +2% | -13% | -8% | -3% | -6% | 0%
This analysis is based on data from 6 locations: Bridge Street, Fitzroy Street, Market Hill, Rose Crescent, Regent Street and Sidney Street.
Notes: Source: Cambridge BID footfall data.
Technical note: Data from the following locations: Bridge Street, Fitzroy Street at Waitrose, Market Hill, Regent Street, Rose Crescent, Sidney Street. Excludes data for King’s Parade and One Station Square. Table calculations do not include bank holidays, school holidays or any other "non neutral" days. The percentage changes are designed to reflect change on a "typical" day.
Commentary: Most days of the week show a negative change to pre-COVID (June 2019) levels. The largest negative change was a decrease of 5% on Thursday.
Tuesday footfall figures were most recovered compared to June 2019, with a 6% increase.
Wednesday and Thursday are the only days of the week which present lower footfall volumes than this time last year (June 2024).

## Slide 36: Car Parking

## Slide 37: Car Parking: Daily Use
Cambridge multi-storey car park use in September 2025 was 16% below pre-COVID levels and has remained relatively stable over the last 2 years.
Queen Anne Terrace usage is the furthest ahead of pre-COVID (+9%), whilst Grafton East usage is furthest below pre-COVID (-61%).
Pre-COVID to Now: |  | 
September 2019 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-16% | -17% | -15%
2023 to Now: |  | 
September 2023 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
1% | 0% | -1%
Previous year to Now: |  | 
September 2024 to September 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
-5% | -5% | -3%
This analysis is based on data from 5 car parks in Cambridge: Grafton East, Grafton West, Grand Arcade, Park Street and Queen Anne Terrace. Park Street car park closed in Jan 2022 and re-opened in Nov 2024 - usage figures for Park Street are included on this chart so that the impact of its closure and re-opening can be seen.
Park St car park closed for redevelopment (Jan 2022)
Park St car park re-opened (Nov 2024)
Multi-storey car park usage, Cambridge
Notes: Source: Cambridge City Council Car Parking data
Technical notes: Table calculations do not include bank holidays, school holidays, or any other "non neutral" days. The percentage changes are designed to reflect change on a "typical" day. As outlined at the start of this slide pack, 'weekdays' do not include Fridays.
Park Street Car Park re-opened in late November 2024.
Commentary:
Multi-storey car park usage in central Cambridge is 16% below the pre-Covid level of September 2019.
The figures for September 2025 show a small change compared to last year (September 2024). Monday to Thursday figures are 5% below last year, there is also a 3% decrease in Weekend usage.
Generally, the line for 2025 has tracked very similarly to that of 2024 – fluctuating between being slightly above and slightly below the 2024 line at various points in the year.
Additionally, an increased charge for car parks was introduced in February 2023 and may be having an impact on usage compared to any periods in which parking was cheaper.

## Slide 38: Car Parking: Length of Stay by Month
September 2025 average daily usage of multi-storey car parks is 16% lower than pre-COVID, and 5% lower than last year.
The split by length-of-stay has stayed fairly consistent over time.
Multi-storey car park average daily usage by month, split by length of stay
This analysis sums data from 5 multi-storey car parks in Cambridge: Grafton East, Grafton West, Grand Arcade, Park Street and Queen Anne Terrace. Park Street car park was closed from Jan 2022 and re-opened in late Nov 2024 - usage figures for Park Street are included on this chart so that the impact of its closure and re-opening can be seen.
Notes: Source: Cambridge City Council Car Parking data
Technical notes: School holidays, bank holidays and any other "non neutral" days are not included in calculations for this chart.
Commentary:
The proportionate split in length of stay in Cambridge's multi-storey car parks is relatively consistent across the four months shown within the chart.
The chart indicates that September 2025 usage is similar to 2023 and slightly below 2024, but overall volumes are still below that which was seen in 2019.
Caveats with this chart are that Park Street Car park closed in January 2022, and a new car park charge was introduced in February 2023.
Park Street Car Park re-opened in late November 2024.

## Slide 39: Car Parking: Length of Stay by Car Park
Multi-storey car park usage by site and length of stay (September 2025)
In September 2025, Grafton West had the highest proportion of stays under 3 hours (89%) whilst Queen Anne Terrace had the lowest proportion (60%).
Grand Arcade continues to be the most popular car park despite having a similar number of spaces as Grafton East.
222 spaces
572 spaces
888 spaces
286 spaces
951 spaces
Notes: Source: Cambridge City Council Car Parking data
Commentary:
89% of September 2025 visits to Grafton West lasted less than three hours – making it the most likely facility to be used for short stays.
Queen Anne Terrace is the facility with the highest proportion of long stays, with 40% of September 2025 visits lasting more than three hours.
Grand Arcade is comfortably the most popular multi storey car park facility in Cambridge – with just over 75,000 patrons in June.

## Slide 40: Rail Passengers

## Slide 41: Rail Passengers: Usage
Local station entries and exits are below pre-COVID levels (2018/19) in most districts. South Cambridgeshire is the only district exceeding pre-COVID (+5%), driven by a 56% increase at Cambridge North (the fastest growing station in Cambridgeshire and Peterborough).
Cambridgeshire (incl Pboro)
Pre-COVID to Now:
2018/19* to 2023/24
-12%
Cambridgeshire (excl Pboro)
Pre-COVID to Now:
2018/19* to 2023/24
-14%
District | Cambridge | East Cambridgeshire | Fenland | Huntingdonshire | Peterborough | South Cambridgeshire
Pre-COVID to Now: 2018/19* to 2023/24 | -16% | -11% | -11% | -24% | -7% | +5%
*2018/19 used as the pre-COVID baseline because 2019/20 data is affected by March 2020 being part of the first COVID-19 lockdown.
Notes: Source: Rail statistics, ORR. Table 1415a
Technical note: Rail Passenger annual data runs April – March. 2018/19 is used as the pre-COVID baseline as 2019/20 entries and exit data is affected in March 2020 by the first COVID-19 lockdown.

## Slide 42: One Station Square Footfall
Note:
Concerns were raised regarding the reliability of the One Station Square footfall data following a sudden drop in April 2024. Cambridge BID confirmed that an issue was repaired in December 2024.
Following those repairs, the 2025 data continues to show large fluctuations. Cambridge BID have therefore been asked to check the reliability of the 2025 data.
While these checks are ongoing, the graph will continue to be updated but % change figures will not be provided.
Pre-COVID to Now: |  | 
Excluded due to sensor issues in 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
2023 to Now: |  | 
Excluded due to sensor issues in 2025 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
Previous year to Now: |  | 
Excluded due to sensor issues in 2024 |  | 
Mon-Sun | Weekdays (Mon-Thu) | Weekends (Sat-Sun)
Footfall at One Station Square (outside Cambridge train station), December 2019 to September 2025
Notes: Source: Cambridge BID footfall data​
Technical note: Table calculations do not include bank holidays, school holidays, or any other "non neutral" days. The One Station Square sensor was fitted in December 2019 so pre-COVID data is not available for all months. For March comparisons, we use the first two weeks of March 2020 (1st – 14th) to ensure impacts of the first lockdown are not included, but we acknowledge the comparison is not ideal. Data may be impacted by strike action. As outlined at the start of this slide pack, 'weekdays' do not include Fridays.
The data collected at One Station Square throughout 2024 appears to be erroneous and has therefore been omitted from this slide. Cambridge Bid have confirmed that this footfall counter was repaired in December 2024. Monitoring of this site resumed in January 2025. The 2025 data continues to show fluctuations. Cambridge BID have been asked to comment on the reliability of the 2025 data.
Commentary: Footfall at One Station Square was 43% below pre-COVID levels (February 2020) on weekdays (Monday to Thursday) and 21% below on weekends (Saturday to Sunday). Compared to June 2023, footfall levels were 25% lower in June 2025. Weekdays saw an 21% decrease compared to June 2023, and weekends saw a 28% decrease.

## Slide 43: Bus Passengers

## Slide 44: Bus Passengers Estimates
There are two methodologies for estimating local bus passenger journeys:
Method 1: the bus driver pushes a button when
a passenger boards the bus.
This method of data collection should be more accurate as it captures observed passenger journeys. However, the accuracy of recording varies by driver and may vary over time.
Suggests higher growth in P&R journeys since 2019 (+20%).
Method 2: estimate passenger journeys based on the
no. tickets sold
This method uses assumptions about the no. journeys made per ticket to estimate total passenger journeys. For example, it is assumed that someone purchasing a 1-week ticket will make 10 journeys on average. The method relies heavily on the accuracy of the assumptions used.
Suggests lower growth in P&R journeys since 2019 (0%).
There are positive and negative aspects to each method and one may be more appropriate depending on the use case. For transparency, P&R data using both methods is presented in slides 48-51 to allow a comparison to be made.
Notes: Source: Stagecoach

## Slide 45: Bus Passengers: national stats Method #1 – Driver estimate
Department for Transport statistics show that 18.7 million passengers used bus services in Cambridgeshire from April 2023 to March 2024. This is only 5% below the pre-COVID baseline. Passenger volumes in Peterborough (7.4 million) are 21% below pre-COVID levels but bus journeys per person continue to be higher in Peterborough.
Cambridgeshire:
Total Bus Passengers,
April 2023 – March 2024:
18.7 million
(25 journeys per head of population)
Peterborough:
Total Bus Passengers,
April 2023 – March 2024:
7.4 million
(32 journeys per head of population)
*Pre-COVID is defined as the average of three years (2017-18, 2018-19, 2019-20) to minimise the impacts of the pandemic that were present during the last week of the 2019-20 period.
Source: DfT Annual Bus Operator Survey: https://www.gov.uk/government/collections/bus-statistics
Notes: Source: DfT Bus Statistics: https://www.gov.uk/government/collections/bus-statistics
Bedfordshire figures are compiled by summing those provided separately for Luton, Bedford, and Mid-Bedfordshire in the DfT dataset.

## Slide 46: Bus Passengers: all passengers Method #1 – Driver estimate
In September 2025, bus passenger volumes on services based at Stagecoach’s Cambridgeshire depots (Cambridge and Fenstanton) were 2% ahead of pre-COVID. Meanwhile, bus passenger volumes on services based at the Peterborough depot were 24% lower than pre-COVID.
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
Sept 2019 to Sept 2025
+2%
Cambridge and
Fenstanton depots
Pre-COVID to Now:
Sept 2019 to Sept 2025
-24%
Peterborough
depot
Pre-COVID to Now:
Sept 2023 to Sept 2025
+9%
Cambridge and
Fenstanton depots
2023 to Now:
Sept 2023 to Sept 2025
+1%
Peterborough
depot
2023 to Now:
Due to the commercial sensitivity of this data, bus passenger volumes are not labelled on the y-axis of this graph. Park and Ride services only operate from the Cambridge depot.
This data is estimated by drivers who press a button when a passenger boards the bus.
Bus Passengers
Notes: Source: Stagecoach (Button-push methodology)
Technical note: Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.

## Slide 47: Bus Passengers: non-P&R services Method #1 – Driver estimate
In September 2025, bus passengers on non-Park & Ride services were 2% below pre-COVID at the Cambridgeshire depots (Cambridge and Fenstanton), and 24% below pre-COVID at the Peterborough depot.
Bus Passengers
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
Sept 2019 to Sept 2025
-2%
Cambridge and Fenstanton depots
Pre-COVID to Now:
Sept 2019 to Sept 2025
-24%
Peterborough
depot
Pre-COVID to Now:
Sept 2023 to Sept 2025
+10%
Cambridge and Fenstanton depots
2023 to Now:
Sept 2023 to Sept 2025
+1%
Peterborough
depot
2023 to Now:
Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
This data is estimated by drivers who press a button when a passenger boards the bus.
Notes: Source: Stagecoach (Button-push methodology)
Technical note: Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
Commentary: Bus passenger numbers, excluding passengers who used the park and ride service, continued to rise through 2023 and 2024 but remained below pre-COVID volumes. So far in 2025, figures have tracked similarly with 2024 – and, in more recent weeks, have just fallen slightly below the volumes seen at this point last year.
Passenger numbers gradually decreased in August 2025 before sharply rising again once September began – this tracks with other years, and is to be expected due to school summer holidays.
Note that, In January 2023, the government announced a £2 cap on single tickets (£2 bus fare cap - GOV.UK (www.gov.uk)).

## Slide 48: Bus Passengers: P&R services Method #1 – Driver estimate
Based on driver estimates, Park & Ride bus passenger volumes have increased by 19% since September 2019 and by 5% since September 2023.
Sept 2019 to Sept 2025
+19%
Cambridge sites
Pre-COVID to Now:
Sept 2023 to Sept 2025
+5%
Cambridge sites
2023 to Now:
Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
This data is estimated by drivers who press a button when a passenger boards the bus.
Notes: Source: Stagecoach (Button-push methodology)
Technical note: Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
Commentary: Overall volumes have recovered beyond those seen in 2019 (+19%) – with Madingley and Newmarket park & ride sites experiencing the best recovery pattern of all individual sites. Babraham is still a little lower than pre-COVID, in contrast to other sites. This may be due to solar canopy roof works which have been ongoing at that location recently.
Note that in January 2023, the government announced a £2 cap on single tickets (£2 bus fare cap - GOV.UK (www.gov.uk)).
MAD=Madingley Road P&R
NEW = Newmarket Road P&R
TRU = Trumpington P&R
BAB = Babraham Road P&R
MIL = Milton Road P&R

## Slide 49: Bus Passengers: P&R services Method #1 – Driver estimate
Based on driver estimates, Park and Ride (P&R) passenger volumes are above pre-COVID levels (+19%). All sites are above 2019 volumes except for Babraham Road (-15%) – this may be linked to the solar canopy construction works at Babraham Road P&R Site.
© OpenStreetMap Contributors
All P&R Sites
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+19%
+5%
Madingley Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+54%
+14%
Trumpington P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+30%
+13%
Milton P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+20%
+17%
Newmarket Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+34%
+8%
Babraham Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
-15%
-14%
This data is estimated by drivers who press a button when a passenger boards the bus.
Notes: Source: Stagecoach (Button-push methodology)

## Slide 50: Bus Passengers: P&R services Method #2 – Sales estimate
Using the sales estimate, Park & Ride route usage shows no change compared to pre-COVID (September 2019) but is up by 7% compared to September 2023.
0%
Sept 2019 to Sept 2025
Cambridgeshire sites
Pre-COVID to Now:
Sept 2023 to Sept 2025
+7%
Cambridgeshire sites
2023 to Now:
Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
This data is estimated based on the number of tickets sold and assumptions regarding the no. journeys made per ticket.
Notes: Source: Stagecoach (Multiplier methodology)
Technical note: Due to the commercial sensitivity of this data, bus passenger volumes are not marked on the y-axis of this graph.
Methodology note: multipliers are applied to ticket sales in order to estimate passenger journeys made. These are outlined in full below.
Single – 1 journey.
Concession/Smart – 1 journey.
Return – 2 journeys.
Day – 3.25 journeys.
Mega rider – 10 journeys.
Small Group – 9 journeys.
Large Group – 12 journeys.
Commentary:
Park and ride usage (via ticket sale multiplier methodology) has started to plateau after an increasing trend post-COVID.
Overall usage shows no change compared to September 2019, but is 7% above 2023.
Note that, In January 2023, the government announced a £2 cap on single tickets
(£2 bus fare cap - GOV.UK (www.gov.uk)).
MAD=Madingley Road P&R
NEW = Newmarket Road P&R
TRU = Trumpington P&R
BAB = Babraham Road P&R
MIL = Milton Road P&R

## Slide 51: Bus Passengers: P&R services Method #2 – Sales estimate
Using the sales estimate, Park and Ride (P&R) route usage is very similar to pre-COVID levels (-0%), but up by 7% on 2023. All routes show an increase compared to 2023 except Babraham (PR4), which may be linked to the solar canopy construction works at Babraham Road P&R Site.
© OpenStreetMap Contributors
All P&R Sites
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
0%
+7%
Madingley Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+29%
+16%
Trumpington P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+3%
+7%
Milton P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
-6%
+17%
Newmarket Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
+7%
+8%
Babraham Road P&R
Sept 2019 to Sept 2025
Sept 2023 to Sept 2025
-21%
-5%
This data is estimated based on the number of tickets sold and assumptions regarding the no. journeys made per ticket
Notes: Source: Stagecoach (Multiplier methodology)
Methodology note: multipliers are applied to ticket sales in order to estimate passenger journeys made. These are outlined in full below.
Single – 1 journey.
Concession/Smart – 1 journey.
Return – 2 journeys.
Day – 3.25 journeys.
Mega rider – 10 journeys.
Small Group – 9 journeys.
Large Group – 12 journeys.

## Slide 52: Guided Busway Passengers Method #2 – Sales estimate
A total of 3.8 million passengers used the Cambridgeshire Guided Busway between September 2024 and August 2025.
This is 24% above the preceding 12 months (September 2023 – August 2024) but is 13% below the equivalent period pre-COVID (September 2018 – August 2019).
-13%
Busway Usage (Bus Passengers)
Pre-COVID to Now:
2019 – 2025*
+24%
Busway Usage (Bus Passengers)
Previous Year to Now:
2024 – 2025*
*All figures are for 12 months ending August.
E.g. for 2019 – 2025, the % change reflects the difference between total passengers from September 2018 - August 2019 compared to total passengers from September 2024 - August 2025.
Source: Stagecoach and Whippet. This data is estimated based on the number of tickets sold and assumptions regarding the no. journeys made per ticket.
4.3m passengers
(Sep 2018 – Aug 2019)
3.1m passengers
(Sep 2023 – Aug 2024)
3.8m passengers
(Sep 2024 – Aug 2025)
Notes: Source: Stagecoach / Whippet.

## Slide 53: Micro-mobility

## Slide 54: Voi E-scooters and E-bikes in Cambridge
The use of Voi e-scooters and e-bikes has increased since the same period last year (+29%). Weekday peak usage is consistently seen at 8am in the morning and 5pm in the evening. Riders aged under 40 represent 82% of riders indicating that this mode of transport is less popular with those over 40.
Voi have operated an electric scooter (e-scooter) and electric bike (e-bike) trial scheme in and around Cambridge since October 2020.
Key statistics: July – September 2025
% change from same period in 2024
Number of rides:
+29%
% change from same period in 2024
Number of active riders:
+19%
% change from same period in 2024
Total ride distance:
+31%
% change from same period in 2024
Source: Voi. Note Voi has made a methodological change from June 2025 in the age distribution calculations to better capture e-bike riders who do not need to verify their age with a license.
Notes: Source: Voi

## Slide 55: Air Quality

## Slide 56: Air Quality Monitoring Locations
Continuous Air Quality Monitoring Sites, Cambridge
© OpenStreetMap Contributors
Location | Description
Montague Road | Close to the junction with Elizabeth Way.
Newmarket Road | Close to Cambridge Retail park on Newmarket Road. Data unavailable in early 2025 due to sensor upgrade.
Parker Street | Close to the bus station.
Regent Street | To the West of Parker’s Piece. Site monitors Nitrogen dioxide (NO2) only.
Gonville Place | Near Hill’s Road, South of Parker’s Piece. Inactive from April 2022 to March 2024.
The Cambridge City Council Air Quality team provide data from 5 continuous air quality monitors in central Cambridge. The monitors measure Nitrogen dioxide (NO2) and Particulate Matter (PM10 and PM2.5) which are all proxies for overall air quality.
Notes: Source: Cambridge City Air Quality team. Data for the Cambridge air quality continuous monitors can also be found at: Air quality in England (airqualityengland.co.uk).
Technical note: Please note there may be slight differences between the data on Air Quality in England and data in this pack as air quality data undergoes a ratification process.

## Slide 57: Air Quality: Nitrogen dioxide (NO2)
All the continuous monitoring sites in Cambridge city centre show a decrease in nitrogen dioxide pollution since the June 2017-2019 baseline, in particular Montague Road (-45%). Concentrations of NO2 have seen a decrease since April 2025, in line with usual seasonal trends.
 | Pre-COVID to Now: | 2023 to Now: | Last year to Now:
 | Sept 2017-19 baseline to Sept 2025 | Sept 2023 to Sept 2025 | Sept 2024 to Sept 2025
Gonville Place | -39% | No Sept 2023 data | -7%
Montague Road | -45% | -27% | -22%
Newmarket Road | -27% | +22% | +10%
Parker Street | -37% | +15% | +27%
Regent Street | -28% | +13% | +10%
Overall | -35% | +6% | +4%
Monthly average NO2 concentrations (µg/m3) by site
NO2 is partly generated by road transport. Concentrations are given in micrograms (µg) per cubic metre of air (m3 )
Notes: Source: Cambridge City Air Quality team. Data for the Cambridge air quality continuous monitors can be found at: Air quality in England (airqualityengland.co.uk).
Technical note: Data for the Gonville Place sensor is not available from April 2022 to March 2024. Newmarket Road data is missing between January and March 2025 due to sensor upgrades.
Please note there may be slight differences between the data on Air Quality in England and data in this pack as air quality data is provisional until it has undergone a ratification process.

## Slide 58: Air Quality: Particulate Matter (PM10)
PM10 concentrations have been between 10 and 15µg/m3 since July 2025 which is below the higher levels detected in Spring 2025.
Concentrations decreased slightly in September.
Monthly average PM10 concentrations (µg/m3) by site
 | Last year to Now:
 | Sept 2024 to Sept 25
Gonville Place | -34%
Montague Road | -44%
Newmarket Road | Historic data not yet available
Parker Street | -35%
PM10 is a type of pollution that is made up of particulate matter (all the solid and liquid particles in the air e.g. smoke, dust, pollen). PM10 pollution has larger particles (diameter of 0.01mm or less) and is partly generated by road transport.
Concentrations of PM10 must not exceed an annual average of 40 µg/m3 (Air Quality Standards Regulations, 2010).
Concentrations are given in micrograms (µg) per cubic metre of air (m3 )
Notes: Source: Cambridge City Air Quality team. Data for the Cambridge air quality continuous monitors can be found at: Air quality in England (airqualityengland.co.uk).
Technical note: Please note there may be slight differences between the data on Air Quality in England and data in this pack as air quality data is provisional until it has undergone a ratification process.

## Slide 59: Air Quality: Particulate Matter (PM2.5)
PM2.5 concentrations have been between 4 and 10 µg/m3 since July 2025 which is below the higher levels detected in Spring 2025.
In July, Parker Street saw higher concentrations which decreased in August and September.
Monthly average PM2.5 concentrations (µg/m3) by site
 | Last year to Now:
 | Coming soon
Gonville Place | -48%
Montague Road | -54%
Newmarket Road | Historic data not yet available
Parker Street | -51%
PM2.5 is a type of pollution made up of particulate matter (all the solid and liquid particles in the air e.g. sea spray, smoke). PM2.5 pollution has smaller particles (diameter of 0.0025mm or less) and is partly generated by road transport.
Concentrations of PM2.5 have an annual mean target level of 10 µg/m3 by 2040 (Environmental Targets (Fine Particulate Matter)(England) Regulations 2023).
Concentrations are given in micrograms (µg) per cubic metre of air (m3 )
Notes: Source: Cambridge City Air Quality team. Data for the Cambridge air quality continuous monitors can be found at: Air quality in England (airqualityengland.co.uk).
Technical note: Please note there may be slight differences between the data on Air Quality in England and data in this pack as air quality data is provisional until it has undergone a ratification process.

## Slide 60: policyandinsight@cambridgeshire.gov.uk